## WorldPhone

### Portable Inmarsat Mini-M Satellite Telephone

WorldPhone Office provides access to the international dial-up telephone, fax and data networks. The elegant custom designed case contains antenna and RF in the lid, and the phone unit in the base. The equipment is designed for quick and reliable operation under all conditions. WorldPhone Office is an ideal communication tool for business travellers and field workers.

NERA Worldphone Advantages

#### Key Features

- 4.8 Kbps voice

- 2.4 Kbps Group 3 fax (Hayes compatible interface).

- 3 hours talk time, 50 hours standby.

- Additional outlets for telephone and fax.

- Water resistant phone for outdoor use.

- Rechargeable NiMh battery and charger integrated in phone.

- SIM card for personal mobility management and authentication.

#### Operating Features

- User friendly backlit LCD display with 64x240 dots (8x40 characters).

- Handsfree.

- Multilingual display support.

- Menu select, cursor keys and four softkeys.

- Built-in user friendly phone book.

| Techinical Specifications |
| --- |
| Environmental Conditions |
| Temperature |  |
| Operating |  |
| antenna: | -35°C to +55°C |
| phone: | -25°C to +55°C |
| storage: | -50°C to +80°C |
| Physical Characteristics |
| Antenna and phone folded together for transport: | H=57mm, W=260mm, D=260mm |
| Phone separate: | H=44mm, W=235mm, D=190mm |
| Weight: | 1.4 kg including batteries |
| Interfaces |
| Ext. tel./fax outlets: | 2 x RJ11, 2-wire with echo cancellation and touch-tone dialling |
| Power: | DC power jack w/2 mm center pin 10-32 VDC |
| Data: | D-SUB , 9 pins, RS232 Hayes AT compatible |
| Antenna Unit |
| Size: | H=57mm, D=260mm |
| Weight: | 1.0kg |
| Mounting: | Detachable from telephone unit |
| Power requirements |
| Consumption typical |  |
| receive: | 0.5 W |
| transmit: | 12 W |